## Slide 2
Network Topology and Connectivity
Azure Foundation Architecture and Hybrid Integration Strategy
Purpose: The next sections provide design considerations based on best practices, Microsoft CAF and Accenture team accumulated experiences implementing Azure network architectures. Additionally, the sections addressing design decisions is based on ongoing discovery with Accenture and NewCo team members.

## Slide 3: Assumptions
Prioritizing security from the ground up, no "isolated pockets" of networking without central security.
Hub NVA firewalls act as the route engine, managing traffic flow and inspection for all intra-Azure and hybrid network traffic
NewCo Azure environment will be a "greenfield" deployment
NewCo Azure cloud will be integrated with on-prem network consisting of a shared MPLS and SD-WAN environment that connects all their physical locations back to their data centers.

## Slide 4: Azure Network Topology Strategy
Traditional Hub-Spoke (recommendation) Unmanaged topology with complete control and proven security patterns
Azure vWAN: Managed service with built-in routing, but less granular control
Options: Hub-Spoke Architecture vs Azure vWAN
Traditional Hub-Spoke Diagram
Notes: Not at the Tenant Root Management Group level to support M&A activity.
Traditional Hub-Spoke
Unmanaged topology with complete control and proven security patterns
Azure vWAN
Managed service with built-in routing, but less granular control

## Slide 5
Azure Network Topology Strategy
Production and Non-Production Environments Separation
Environments
Production
Non-Production
Lab/Staging
Notes: Connectivity subscription will contain no application workloads
Transit vnets in Central & East US 2 with ExpressRoute circuits
Gateway Subnet directs all spoke traffic through firewall scale set
Spoke vnets: Flexible subnetting, VM workloads
Automated provisioning via Terraform
Hybrid integration: Data centers connected via SD-WAN/MPLS
ExpressRoute circuits: Prod, Non-Prod, and Lab
Lab environment isolated for safe infra testing
UDRs on every subnet enforce routing to firewall
Gateway route propagation disabled to enforce inspection
Spoke-to-spoke traffic requires firewall traversal and explicit rules

## Slide 6
On-Premises to Azure Hub (regional ExpressRoute Primary and Secondary)
Hub to Hub inter-region connectivity will use FE and BE transit routes via NVAs between hub vnets
Spoke to Hub to Spoke connectivity will use default route to NVA (no direct spoke to spoke peering)
Internet Egress traffic will exit via NewCo Azure hub VNet
Remote Access
Connectivity Architecture
Network Traffic Flows for Consideration

## Slide 7
Design Decisions
Core Infrastructure Subscription - Contains hub vnets, ExpressRoute, CP firewalls, and shared network services
Hub Subnets: Gateway, Firewall, DNS, Bastion
Regional Strategy: Dual-region support with Central US primary and East US 2 secondary
Security Controls: All traffic through hub firewalls, private IP enforcement
Management Structure: Dedicated management group for core infrastructure
Workload Subscriptions - Contains application spoke VNets with peering to hubs
Connectivity Subscription
Key Architectural Core Elements

## Slide 8
Interconnect Architecture
Branch (Edge) to Azure Traffic Flow via ExpressRoute Hub with NVA Inspection
Branch traffic flows through MPLS backbone (AS 25676) using policies (future state) for routing and path optimization
ECX ExpressRoute provides dedicated connectivity from MPLS to Azure Hub for inspection
Hub-and-spoke architecture routes traffic from Azure Central Hub to Spoke VNet workloads
Notes: network traffic flow analysis
step 1: branch office to mpls
traffic originates from the branch office with an edge router
sd-wan policy is applied at the branch level for traffic classification and routing step 2: mpls backbone transit
traffic traverses the mpls backbone (as 25676) using bgp/isis core routing
the backbone connects pe-1 and pe-2 provider edge routers
bgp routing determines the optimal path through the service provider network step 3: expressroute connection
traffic exits the mpls backbone and enters microsoft's expressroute in the central region
this provides a dedicated 1 gbps circuit with microsoft peering
expressroute offers predictable bandwidth and lower latency compared to internet routing step 4: azure hub vnet processing
traffic enters the azure hub vnet (central)
flows through the er gateway in the gatewaysubnet
security inspection occurs at the checkpoint vmss firewall cluster
route server (routeserversubnet) manages dynamic routing between on-premises and azure
internal load balancer distributes traffic as needed step 5: hub-to-spoke connectivity
vnet peering connects the hub to the spoke vnet
traffic reaches the workload subnet where the application workload resides
sd-wan policy configuration
the diagram shows sophisticated cisco sd-wan policies: application-aware policy: with preferred color gold for priority treatment control policy: routes azure central prefixes path selection criteria: ensures optimal routing with thresholds for loss, latency, jitter, and bandwidth this architecture provides application traffic with built-in redundancy, security inspection, and optimized routing policies.

## Slide 9
Design Decisions
ECX serves as primary interconnect leveraging Cloud Exchange for Azure ExpressRoute circuit
Physical Circuit Isolation/Diversity: engineer dual ExpressRoute circuits with physical geographical diversity Equinix facilities) into MSEE points of presence (POPs)
Implement a bow-tie topology by cross-connecting dual Azure Express Route circuits from distinct MSEE regions to Azure transit domain, each circuit can reach either hub. Support a FE and BE VNets between hub regions with NVA inspection in path
VRF-Based Routing: Ingress traffic from SD-WAN managed MPLS core is routed into Azure via a dedicated VRF instance for traffic isolation / separation
Subnet-Specific Matching: The ingress path is configuration match traffic destined for subnet x.x.x.x, for control, allowing SD-WAN to direct traffic flow towards Azure.
SD-WAN Azure Labels for Policy Enforcement: A label is applied to the traffic entering Azure cloud policy enforcement.
Interconnect Architecture
Key Architectural Core Elements

## Slide 10
Private interconnect via Equinix Fabric: ECX/Fabric L2 (802.1q) platform for private connect to Azure Express Route and OCI Fast Connect (and other clouds)
Separate VRFs per cloud (prod/dev) environments distinct virtual circuits; route leaking can happen at NVA
Azure BGP custom communities provide Azure specific routing intelligence; target specific Azure regions
Interconnect Architecture
Multi-Cloud Interconnect Considerations

## Slide 11: NVA Strategy
Checkpoint NVA VMSS
Design Recommendations
FortiGate NVA VMSS

## Slide 12
Alternate Option
NVA Strategy
Check Point VMSS for scalable, security, policy management.
VMSS in hub VNets auto-scaling based on traffic demand
Azure Firewall NOT considered due BGP peering functionality
OR
FortiGate VMSS
Works with Cisco SD-WAN policies, Zscaler native integration for L7
Terraform, REST API and Ansible modules enable IaC deployments
eBGP peering with Azure Route Server route exchange between on-prem MPLS core(s)
VMSS scaling based on metrics (CPU, memory, session count, etc)

## Slide 13
Deploy DNS forwarder VMs in Hub VNet, configure conditional forwarding to on-premises
Azure private DNS zones to all VNets
Design Considerations
Azure DNS Services

## Slide 14
Option 1: Internet Egress via NewCo Azure Cloud (Recommended)
  This solution provides immediate access to established security policies, threat intelligence, and logging (via NVA) deployed in Azure
Option 2: Internet Egress via NewCo SDWAN DIA:
  This solution provides access to established security policies, threat intelligence, and centralized logging infrastructure deployed on-prem with SD-WAN control
Option 3: NewCo Internet Egress via Existing OldCo DIA
  NewCo workloads leverages existing NewCo Azure tenant internet egress points (Azure OldCo) for outbound connectivity rather than establishing dedicated internet breakouts
Internet Egress
Design Considerations

## Slide 15
Azure Front Door with Private Link (PL) and spoke LB
No hub transit for Internet ingress or hair-pinning through NVAs
Security at the edge using WAF
Traffic uses Microsoft backbone
Anycast edges for availability and failover.
Internet Ingress Strategy (Post-TSA)
Design Considerations
Notes: Azure Front Door with Private Link (PL) and a load balancer in the spoke; origin/source set to PL only.
Security at the edge using WAF; attack prevention before reaching Azure
Traffic uses Microsoft backbone; Anycast edges for availability and failover.
Anycast edges for availability and failover.

## Slide 16
Remote Access

## Slide 17
Remote Access

## Slide 18
Observability and Monitoring
Core Elements
Option 1: Hybrid Extension of On-Premises Solution​
Federated Monitoring with the existing monitoring stack: Extend current Prometheus/Grafana/Splunk infrastructure to Azure through Azure Monitor integration and Prometheus federation to exporter/collectors Azure​
​Option 2: Azure-Native Observability with Hybrid Integration​
Implement Azure Monitor, Log Analytics, and Application Insights platform for all Azure resources with data federation to on-premises Splunk/Prometheus. ​
This design consideration utilizes native Azure capabilities, automated scaling insights, and integration while implementing custom logic apps and Azure Functions to replicate critical metrics to existing Prometheus instances

## Slide 19
Spoke to Spoke Encryption - TLS for hub-to-spoke and spoke-to-spoke traffic
On-Premises to Cloud Encryption - ExpressRoute with additional TLS layer
Cross-Tenant Security Enforcement - Mandatory encryption for NewCo/OldCo tenant services
Azure Key Vault - Centralized management
Check Point performs TLS/SSL inspection
Network Encryption
Core Elements

## Slide 20
Network Segmentation Strategy | Implementation Details
Hub-Spoke Isolation with Centralized Security | All spoke vnets connected to hub through vnet peering with User-Defined Routes (UDRs) forcing traffic through Check Point CloudGuard VMSS firewalls for inspection, logging, and policy enforcement before reaching destinations
Zero Trust Spoke-to-Spoke Communication | Direct spoke-to-spoke connectivity prohibited through disabled gateway route propagation and explicit firewall rules required for any inter-spoke communication, ensuring complete traffic visibility and granular access control
Environment-Based Network Boundaries | Production and non-production environments maintained in separate hub vnets with dedicated ExpressRoute circuits and firewall instances, preventing cross-environment traffic except through approved firewall policies with comprehensive audit logging
Private IP Enforcement and Public Access Control | Azure Policy prohibits public IP creation on resources with all internet egress routed through hub firewalls via 0.0.0.0/0 UDR configurations, while internet ingress limited to specific application spokes through Azure Front Door with WAF integration
Network Segregation Strategy
Core Elements

## Slide 21
Questions and Feedback

## Slide 22
Next Steps

## Slide 23
Multi-Cloud Visibility
For unified Azure / Oracle / On-Prem documentation
Future state, business goals modeling and capacity planning.
Model relationships across Azure subscriptions and management groups
Single view of clouds ER/FC circuits and Equinix cross-connects. Right size circuits
DNS modeling for on-prem and Azure cloud resolution chains
NetBox
Design Considerations
Recommendation

## Slide 24
Observability Strategy
NetBox
Topology aware
Dynamic network Monitoring

## Slide 25
Traditional Hub and Spoke: Selected over Azure vWAN for complete control
Dual Regional Design: Central US (primary) and East US 2 (secondary)
VRF Segmentation: Azure as distinct VRF for routing isolation
Zero Trust Design: Security-first architecture from day one
Equinix Cloud Exchange: Primary interconnect for ExpressRoute and OCI
Dual ExpressRoute: Physical diversity with bow-tie topology
Cisco SD-WAN Integration: Catalyst overlay with 8000V edge devices
Site-to-Site VPN: Backup connectivity for resilience
Check Point CloudGuard VMSS: Auto-scaling firewall clusters
Private IP Enforcement: Azure Policy prohibits public IPs
TLS 1.3 Encryption: All traffic flows encrypted in transit
Centralized Inspection: All traffic through hub firewalls
Infrastructure as Code: Terraform primary, Bicep/ARM as alternatives
Pipeline Deployment: Automated CI/CD with gates and approvals
Subscription Vending: Standardized provisioning workflows
Policy as Code: Governance automation and drift prevention
Core Infrastructure Subscription: Hub VNets and shared services
Workload Subscriptions: Application spoke VNets
Management Groups: Core Infra, Production, Non-Production
Policy Enforcement: Automated governance and compliance
Hybrid Monitoring: Extend Prometheus/Grafana or Azure-native
Log Analytics Consolidation: Reduce from 17 to fewer workspaces
Network Watcher: Azure-native network monitoring
SIEM Integration: Existing Splunk or Azure Sentinel options
Network Architecture Foundation
Azure Network Topology Strategy
Security Architecture
Observability Strategy
Management Structure
Automation Deployment
Connectivity Infrastructure
Core Elements
Appendix

## Slide 26
NVAs are security transit points to/from both regions with inspection at ingress and egress FE and BE vnet peering
Aligns with NIST zero trust model for continuous resource identification and CAF workloads using identity, policy, security controls
Central boundary security and segmentation with policies, monitor and control communications at external/internal boundaries, enforce approved info flows
FE can failover (no BE impact), replication can be send over single vnet instead so not impact day to day prod workloads
Internet traffic only on FE vnet
Region to Region Architecture Strategy
Design Considerations
Recommendations are based on compilation of NIST (SP 800-207) and CAF guidelines

## Slide 27
Remote Access
ZScaler Hub VNet Deployment

## Slide 28
Option 1: Hybrid IPAM with Gradual Azure Native Transition
Phased IPAM Migration Strategy: Maintain Infoblox as the authoritative source for all IP allocations during initial Azure deployment as a secondary system for cloud-native subnet management.
Option 2: Azure Native IPAM with Infoblox Integration
Azure IPAM as Primary with Infoblox Federation: Implement Azure as the primary IP address management platform for all cloud resources while maintaining Infoblox integration for on-premises DNS/DHCP services
Use API for synchronization. This design decision provides centralized visibility and integrates well with PowerShell/Terraform automation pipelines
IP Addressing and Management
Design Considerations

## Slide 29
Site to Site VPN (can be used as backup for telco delays)​
Internet Ingress traffic

## Slide 30
Hub-and-Spoke Architecture – A traditional Azure topology where a central hub VNet provides shared services (firewalls, gateways) to multiple spoke VNet hosting workloads.
Azure vWAN (Virtual WAN) – Microsoft-managed networking service with simplified routing and connectivity, but less granular control compared to hub-and-spoke.
ExpressRoute – A private, dedicated connection between on-premises infrastructure and Azure, offering predictable latency and reliability compared to internet VPN.
Site-to-Site VPN – Secure IPsec tunnel between on-premises networks and Azure VNets, often used as a backup to ExpressRoute.
Equinix Cloud Exchange (ECX) – Interconnection service used to link Azure ExpressRoute circuits with other clouds or on-premises networks.
SD-WAN (Software-Defined WAN) – Overlay technology that uses software policies to manage connectivity across MPLS, internet, and cloud networks.
Check Point CloudGuard VMSS – Cloud-native firewall solution deployed as a Virtual Machine Scale Set for scalable security enforcement in Azure.
NVA (Network Virtual Appliance) – Virtualized network function (e.g., firewall, router) running in Azure for traffic inspection and routing.
UDR (User-Defined Route) – Custom route table in Azure that forces traffic through a specific path, typically through a firewall.
VRF (Virtual Routing and Forwarding) – Logical routing table segmentation for traffic isolation across multiple tenants or environments.

## Slide 31
Zero Trust – Security model that assumes no implicit trust; all traffic must be verified, inspected, and explicitly allowed.
TLS 1.3 – Latest version of Transport Layer Security, ensuring data encryption in transit.
Azure Key Vault – Managed service for secure storage and management of cryptographic keys and certificates.
Observability – End-to-end monitoring strategy using metrics, logs, and traces (e.g., Prometheus, Grafana, Azure Monitor, Log Analytics).
L2 802.1Q - Ethernet standard that adds a small “tag” so multiple isolated networks (VLANs) can share the same physical link.